PERIODIC MAINTENANCE/SERVICE	For 4-wheel drive vehicles

Christophe Humbert Inter Aide Ethiopie 19.05.2008

Mini Service “A”: Every 5 000 km is sufficient

- Clean the engine

- Change the oil filter and engine oil

- Clean and drain the water sedimentary

- Clean the air cleaner and its dust sedimentary (compressed air + washing as per instruction on the filter)

- Check the oil level gearbox, transfer box. Axles check for water in the axles (if water mixed in, change the oil).

- Check the condition of the suspension: insulation (rubber bushes), spring blades and Shock absorbers (and their bushing).

- Clean the axle breathers box axles union and hose. Grease the transmission and Steering system (8 nipples), tight the steering ball joints if necessary.

- Check the condition of the rear and the front engine mountings.

- Check the condition of the exhaust pipe and the insulters (rubber mounting).

- Check the condition and tension of the belt

- Check the different warning lights of the dashboard.

- Check the tightness in front wheel hubs and front axle swiveling boxes by

Shaking strongly the front wheels

- Check the tightness in the steering system

- Check the pads or shoes of the front breaks and correct if necessary.

- Check the hood bushings adjustment (hood should not move when closed)

B Every 15 000 km

- Change the diesel filter.

C  Every 25 000 km

- Change oil gearbox transfer box, axle

- Grease hinges and locks of doors.

- Grease tilt mechanic of steering system.

- Change the tires when necessary

- Change the air cleaner when necessary

- Balance the front wheels when steering checks at 80 KM/H

Check every day:

- Before starting check the engine oil level

- The coolant level

- The steering fluid, the clutch and brake fluid level